## Slide 1: McRTOS A Multi-core RTOS
Germán Rivera

## Slide 2: McRTOS Features Overview
Preemptive kernel
Round-robin scheduler with priorities (and O(1) scheduler)
Nested interrupts support
Mutexes with priority inheritance (priority boosting) to prevent unbounded thread priority inversion
Condition variables instead of semaphores
Software timers use a timing wheel algorithm for efficient timer start, timer bookkeeping and timer stop.
Multi-core support for “static” SMP
Application threads run in unprivileged mode (ARM User mode) and McRTOS kernel runs in privileged mode (ARM System and IRQ modes).
System call interface to protect access to McRTOS kernel services
McRTOS APIs accessible to application threads via system calls. APIs return and receive pointers to opaque objects as parameters to prevent applications from tampering McRTOS internal data structures.
First failure data capture (FFDC) support

## Slide 3: McRTOS API Philosophy
For the sake of determinism, static is better than dynamic:
  Application thread architecture must be defined statically at compile-time
  Threads should not be created/terminated dynamically
  Threads should terminate only due an error
    Thread creation API no exposed by default
    Threads can be terminate themselves only by calling a "thread abort" API and
  aborted threads cannot be recycled for creating new threads
  Mutexes, condvar, timers and other McRTOS resources should not be created/destroyed dynamically
    Resource creation APIs not exposed by default
    No resource destruction APIs provided
  Static SMP support:
    Threads cannot migrate fro one core to another
Mutexes and condvars can only be used to synchronize threads running in the same core (if needed, inter-core communication can still be done using inter-processor interrupts and shared memory)
Opaque object pointers are returned and received by McRTOS APIs

## Slide 4: Lesson of Humility
Having a clean and elegant design and code does not mean you can claim victory early.
  The nastiest bugs are not major design mistakes but subtle and often trivial low-level/assembly coding bugs, that can easily cripple the reliability of the entire software no matter how carefully thought the design and elegant the code may be.

## Slide 5: Lesson of Humility (2)
These trivial almost insignificant bugs can cause a lot of debugging time, but ironically their fix is a one line change.
  Some nasty bugs that caused my a lot of debugging time:
    An "atomic increment" assembly routine for pointers to structures did not specify the size of the pointer, so only incremented one byte, instead of the structure size
    interrupt stack too small
      Imprinting the stack ands having "buffer zone" of at least one word at the
    top end of the stack helped debug this
    incorrect assembly instruction in context switch: ldmia r1, {r0-r12, lr, pc}^
      Caught this thanks to the following assert:
        FDC_ASSERT_VALID_CODE_ADDRESS(cpu_lr_register);
        However this assert is wrong in general as the compiler may generate
      Code to use LR as a scratch register in the middle of a routine
    Blindly switching back to the interrupted CPU mode in an ISR to capture the interrupted context SP and LR. This is wrong if interrupted CPU mode is user mode, as there is no way to switch to IRQ mode from user mode by using msr (the nasty thing is that the processor does not generate an undefined instruction for this "msr" instruction, it just seems to ignore the instruction)

## Slide 6: McRTOS Source Code Size
  PS> wc -l .\src\McRTOS\*.s
  182 .\src\McRTOS\McRTOS_crt_armv4.s
  313 .\src\McRTOS\McRTOS_interrupt_service_routines_armv4.s
  635 .\src\McRTOS\McRTOS_kernel_services_armv4.s
  301 .\src\McRTOS\McRTOS_system_call_wrappers_armv4.s
  117 .\src\McRTOS\run_time_exception_handlers_armv4.s
  1548 total
  PS> wc -l .\src\McRTOS\*.c
  863 .\src\McRTOS\failure_data_capture.c
  366 .\src\McRTOS\generic_list.c
  489 .\src\McRTOS\McRTOS_execution_controller.c
  2377 .\src\McRTOS\McRTOS_kernel_services.c
  875 .\src\McRTOS\McRTOS_startup.c
  533 .\src\McRTOS\utils.c
  5503 total
  PS> wc -l .\inc\McRTOS\*.h
  215 .\inc\McRTOS\arm_defs.h
  94 .\inc\McRTOS\compile_time_checks.h
  695 .\inc\McRTOS\failure_data_capture.h
  283 .\inc\McRTOS\generic_list.h
  488 .\inc\McRTOS\McRTOS.h
  168 .\inc\McRTOS\McRTOS_config_parameters.h
  762 .\inc\McRTOS\McRTOS_internals.h
  891 .\inc\McRTOS\McRTOS_kernel_services.h
  16 .\inc\McRTOS\McRTOS_system_calls.h
  116 .\inc\McRTOS\utils.h
  3728 total

## Slide 7: McRTOS High-level Architecture

## Slide 8: McRTOS Sartup Sequence

## Slide 9: McRTOS Tick Timer Interrupt

## Slide 10: McRTOS System Call Sequence

## Slide 11: McRTOS Synchronous Context Switch when Acquiring a Mutex

## Slide 12: McRTOS Synchronous Context Switch when Releasing a Mutex

## Slide 13: McRTOS Major Data Structures

## Slide 14: McRTOS LPC2478-STK RAM Map